## Slide 1: In Lecture 1, we introduced Laplace transforms. Today we will finish Laplace transforms and begin our study of inverse Laplace transforms.
Lecture 1 – Laplace Transforms
Laplace transform is a linear integral transformation taking functions from the time domain () to the Laplace domain ().
The Laplace variable is a complex number, the real part of which quantifies energy absorption and the complex part of which quantifies oscillation frequency.
Exponential function – energy absorption
Sine function - oscillation
Lecture 2 – Laplace/Inverse Laplace Transforms
Laplace transform table examples
Laplace transform of the time derivative(s) of a function
Initial Value Theorem and Final Value Theorem
Application to terminal velocity problem
Inverse Laplace transforms
Time Domain
Laplace Domain
Goal: Use Laplace transforms to solve differential equations. For example …
First Order
Second Order
?
?

## Slide 2: Example 3: Find the Laplace transform of the sine function .
Step 1: Definition of sine
Step 2: Use linearity of Laplace transform
Step 3: Use Laplace transform of exponential
Step 4: Combine terms by multiplying by complex conjugates

## Slide 3: Example 3: Find the Laplace transform of the sine function .
Step 1: Definition of sine
Step 2: Use linearity of Laplace transform
Step 3: Use Laplace transform of exponential
Step 4: Combine terms by multiplying by complex conjugates
Roots of Denominator Polynomial?
Roots are imaginary
Imaginary part of Roots of Denominator Polynomial – Energy Conservation/Oscillation

## Slide 4: What is the practical importance of the different inputs? How are they generated?
Instrumented Hammers - Impulse
Shaker table – sine (and other)

## Slide 5: The procedure for analyzing dynamic systems is to make a lumped-parameter model of a “real” system, develop differential equations of motion for the model, and solve using Laplace/Inverse Laplace transforms.
Partial Fraction Expansion

## Slide 6: The Laplace transforms of many common functions are known and summarized in tables.
Example 1 – Find the Laplace transform of .

## Slide 7: The Laplace transforms of many common functions are known and summarized in tables.
Example 2 – Find the Laplace transform of .

## Slide 8: The Laplace transforms of many common functions are known and summarized in tables.
Example 3 – Find the Laplace transform of .
Z
Z

## Slide 9: Example 4: Show that the following is true using the definition of the Laplace transform and integration by parts.
Step 1: Apply the definition of the Laplace transform
Step 3: Make definitions
Step 2: Recall integration by parts
Step 4: Apply integration by parts
Can also show …
Initial Conditions

## Slide 10
Let define then we have
Recall , then we can have

## Slide 11: You can go “up” and “down” the Laplace transform table knowing that is the time derivative and is the integral.

## Slide 12: The Initial Value Theorem and the Final Value Theorem are used to analyze time domain behavior without inverting the Laplace transform.
Initial Value Theorem: If the function is bounded and exists, then the following is true.
This provides information about the starting point of a time domain function from its Laplace representation
Final Value Theorem: If the function is bounded and exists, then the following is true.
This provides information about the ending point of a time domain function from its Laplace representation

## Slide 13: Let’s look again at the terminal velocity problem and use what we have learned.
Newton’s Second Law
Resistance Force Proportional to Velocity
Apply Laplace Transform
Inverse Laplace transform
Initial Value Theorem
Final Value Theorem
Notes: https://www.youtube.com/watch?v=ElpqPZd1RJU

## Slide 14: The Laplace transform is applied to linear ODEs, the solution is obtained algebraically in the Laplace domain and then the time domain solution is obtained with the inverse Laplace transform.
First Order Linear ODEs Lead to Laplace Functions of the Following Form
Second Order Linear ODEs Lead to Laplace Functions of the Following Form
The Roots of the denominator polynomial determine the most efficient method to invert the Laplace transform and the form of the solution (oscillatory or exponential).
Use Entry 6

## Slide 15: Example 5: Find the inverse Laplace transform of
Step 1: Factor out the 4 in the numerator and the 5 in the denominator.
Step 2: Use linearity of the inverse Laplace transform.
Step 3: Use table entry 6 in the Laplace transform table.
Comment: Suppose . The solution is UNBOUNDED.

## Slide 16: For second order denominator polynomials , the roots of the denominator polynomial determine the form of the inverse transform.
Second Order Problem
The denominator polynomial is . There are three possibilities.
Real Distinct Roots . Partial fractions expansion and entry 6.
Real Repeated Roots . Partial fractions expansion and entries 6 and 7.
Complex Roots . Complete the square and use entries 20 and 21.

## Slide 17: Example 6: The following problem is from RealizIT.
Step 1: Factor out the 12 in the numerator and the 18 in the denominator.
Step 2: Find the roots of the denominator.
Step 3: Factor and complete a partial fractions expansion.
Step 4: Find and by multiplying through by the denominator and strategically choosing values for s.
=
=
Note that since is a variable, the values of and must be consistent with any values of . Thus we can choose to aid in finding and .

## Slide 18: Example 6: The following problem is from RealizIT.
Step 5: Put in and .
Step 6: Apply table entry 6 to both terms and simplify 51/48 to 17/16.
Real roots of lead to and exponential, non-oscillatory time domain function.
Enter the answers in fractional form. We have worked to be sure that these all come out with even numbers and relatively simple fractions.

## Slide 19: Example 7: The following problem is from RealizIT.
Step 1: Factor out the 7 in the numerator and the 9 in the denominator.
Step 2: Find the roots of the denominator.
Step 3: Complete the square in the denominator.
Step 4: Use table entry 21.
Complex roots of lead to a decaying oscillatory time domain function.

## Slide 20: Partial Fraction Expansion
When using Laplace to solve LTI ODEs, the solution to the ODE in the Laplace domain is a ratio of polynomials in s.
Let where and are polynomials in
Partial fraction expansion helps to solve for
We write
where and are complex numbers.

## Slide 21: The main points of Lecture 2 are given.
Laplace transform tables summarize the Laplace transform of many common functions.
The properties of Laplace transforms used in conjunction with the tables allow us to find the Laplace transforms of many other functions.
For this course, the Laplace transform table it sufficient to all that we do.
The Initial Value Theorem (IVT) and Final Value Theorem (FVT) allow us to deduce the behavior of a time domain function from its Laplace domain representation .
The Laplace transform of the time derivative of a function naturally leads to solutions in the Laplace domain that consist of ratios of polynomials in .
First order linear ODEs Second order linear ODEs
First order systems lead to exponential solutions.
Second order systems lead to exponential solutions if the roots of are real and distinct and lead to exponentially decaying oscillatory solutions if the roots of are complex.
Goal: Use Laplace transforms to solve linear first and second order ordinary differential equations.

## Slide 22: Some notes…
If , then N(s is exactly proper.
If , then N(s is strictly proper.
Roots of N(s are . They are called zeros.
Roots of D(s are . They are called poles.

## Slide 23: Case #1: All roots are separate.
if n=m or if m<n. , are called residues.
How do we solve for the residues?
Example 5: What is the partial fraction expansion of ?

## Slide 24
Find : because m=1<n=2
Find : Multiply (1) by and evaluate at
Find : Multiply by and evaluate at

## Slide 25: What if some roots are complex?
Example 6: What is s the partial fraction expansion of
Find : because n=m=3
Solution
Find : Multiply by and evaluate at

## Slide 26
Find Multiply (1) by and evaluate at
Therefore,
Find Multiply (1) by and evaluate at
Simplification

## Slide 27
To find note that
Then,

## Slide 28: Case #2- has repeated roots
where . The partial fraction expansion is given by
Example7: What is the partial fraction expansion of

## Slide 29
Find because .
Find Multiply (1) by .
Evaluate (2) at .
Find : Multiply (1) by and evaluate at .

## Slide 30
Find : Differentiate (2) with respect to .
Evaluate at
Therefore,

## Slide 31
To find note that
Thus,